## Slide 1
Dual Failure Resiliency on Single Failure Protected Packet Optical Integrated Networks
Zhicheng Sui1, Victor Yu Liu2
Huawei Technologies Co., Ltd.
1Shenzhen, China, 2Santa Clara, CA, USA

## Slide 2: Contents
Motivations:
  Dual-Failure Restorability on Existing Two-Layer Networks
Existing Protection Techniques for Single and Dual Failures
Dual-Failure Resiliency Simulation on Single Failure Protected Two-Layers
Result Analysis
Future works

## Slide 3: Motivations
What Restorability on Dual Failures on Two-Layer Networks
Why Enhanced Service Reliability
  Single failure might not be enough
  Dual Failures, disaster recovery, etc.
Need Two-Layer Protection Coordination?
Source: J. P. Fernandez-Palacios, et. al., IP and Optical Convergence: Use Cases and Technical Requirements, Jan. 31, 2014.

## Slide 4: Topology Connectivity for single or dual failure
Protect single failure is commonly available
  bi-connected topology
  Ring, multi-ring
Protect dual failure
  Tri-connected topology
  full-mesh, partial-mesh
Dual failure best-effort disjoint
  partial tri-connect with cut-pairs
  more than 1 backup paths

## Slide 5: Protection and Restoration
Protection
Working path
Backup path
Shared Capacity
Working path
Backup path
Working path
Dedicated Protection
  Pre-plan path and resource, 1+1/1+1+1
  Fast recovery upon failure, e.g. 50ms
Shared Backup Path Protection (SBPP)
  Reduces capacity used by sharing among backup paths
  Slower recovery than dedicated protection, 1:1/1:1:1
Dynamic Restoration
  Dynamic calculate path and resource after failure
  not guaranteed path or resource, IP dynamic convergence

## Slide 6: Protection of Dual Fiber-Cuts – SBPP
SBPP – Two backup paths protect one working path
  Three paths: mutually link disjoint
  Topology: tri-connected
  Minimize capacity by sharing among dual-failure cases
1
2
3
4
5
6
2
1
2
3
4
1
Working path
Secondary backup path
Primary backup path

## Slide 7: Protection of Dual Fiber-Cuts – Benefit
Significantly reduced redundancies
Protection | Primary Backup Path | Secondary Backup Path | Redundancy
1+1+1 | Dedicated | Dedicated | 313–400%
1+1:1 | Dedicated | Shared | 187–310%
1:1:1 | Shared | Shared | 96–180%
1+1 | Dedicated | n.a. | 130-200%
1:1 | Shared | n.a. | 33-50%
Source: V. Y Liu, D. Tipper “Spare capacity allocation using shared backup path protection for dual link failures,” Computer Communications, special issue on reliable network services, vol. 36, no. 6, March 15, 2013, pp. 666-677. http://dx.doi.org/10.1016/j.comcom.2012.09.007.

## Slide 8: Protection of Dual Fiber-Cuts – SBPP Partial Disjoint Paths
Problem – Lot of backup paths, with shared spare capacity
Results: Overall redundancy does not increase much
Source: V. Y. Liu, D. Tipper, “Spare Capacity Allocation Using Partially Disjoint Paths for Dual Link Failure Protection.” In 9th International Workshop on the Design of Reliable Communication Networks (DRCN), Budapest, Hungary, pp. 171-178, March 4-7. 2013.

## Slide 9: Multi-Layer Protection
Various Combinations
Source: R.G. Prinz, A. Autenrieth, and D.A. Schupke, “Dual failure protection in multilayer networks based on overlay or augmented model,” in International Workshop on Design of Reliable Communication Networks (DRCN), Island of Ischia, Naples, Italy, Oct. 16–19 2005.
Single Layer Scheme
Single Layer Scheme with SRLG disjoint needs
Two Layer Coordination

## Slide 10: Simulation Study for Two Single-Failure Protected Layers
Enough capacity in each packet link for the traffic flows, so minimize the packet links number and optical channel number
1. Traffic Demand Matrix
Optical Topology
2. Packet Topology Planning
3. Packet Link Mapping
Packet Topology SHAPE & rough packet capacity of minimal Packet CAPEX
SURVIVABLE Packet Topology Minimize both Packet & Optical CAPEX
4. What-if Analysis
Simulate scenarios impacted by failures & analyze the results
Failure scenario
what are the dual failure resiliency level on current single failure protected two-layer networks?
Are there any way to improve dual failure resiliency and how about the redundancy?

## Slide 11: Packet Topology Planning & Link Mapping
Traffic Demand Matrix
Packet Topology Planning
Determine TRUNK packet links by traffic matrix
Traffic grooming for minimal packet CAPEX (PHY, VLAN)
Find packet topology SHAPE & rough capacity
Minimize packet CAPEX
Packet Link Mapping
Packet Topology
Check the connectivity of packet topology
Augment to 2-connect packet topology with minimal packet CAPEX
packet link mapping to optical topology & modify for survivability
Optical Topology
0 or 1 or 2 connectivity topology
Minimize Packet CAPEX
Minimize Packet & Optical CAPEX
Get minimal CAPEX SURVIVABLE packet topology
Packet topology mapping using SMART algorithm in [7].
Source: [7] M. Kurant and P. Thiran, “Survivable Routing of Mesh Topologies in IP-over-WDM Networks by Recursive Graph Contraction,” IEEE Journal on Selected Areas in Communications, vol. 25, no. 5, June 2007
2. Packet Topology Planning
3. Packet Link Mapping
1+1 path protection for all packet links
Notes: 背后的客户理解的逻辑: 输入输出—约束—原则—追求的目标—grooming产生的结果
1、输入是初始的物理拓扑、流量矩阵，输出的是初始IP拓扑。
2、IP拓扑Planning的目的是：根据业务矩阵与物理拓扑规划满足客户要求的最优IP拓扑/IP links

## Slide 12: Survivable Packet Topology Mapping
Topology mapping is shown in the interlayer information matrix H
  Links/nodes are indexed numerically/alphabetically
  1 indicates the upper link has its path over the lower link
Survivable Topology Mapping is to optimize H to
  Guarantee the upper layer connected under any single lower failures
  Minimize total capacity used at the lower layer
Columns are indexed by lower layer links
Rows are indexed by upper layer links
Source: Eytan Modiano and Aradhana Narula-Tam, "Survivable lightpath routing: a new approach to the design of WDM-based networks," IEEE Journal of Selected Areas in Communication, May 2002.

## Slide 13: Packet Survivable topology mapping for single fiber failure
Two packet link protection schemes in optical topology: (1) no protection or restoration; (2) 1+1 path protection;
Optical
Lone Island
Still connected
Island cut set
Packet
1+1
1+1
Topology constraint but not capacity constraint is considered
Cut-pair dual-failure scenario is ignored
Flows were restored on residual packet layer topology after two fiber cuts under (1) or (2)

## Slide 14: 4. What-if Analysis
What-if analysis
Identify input failure objects: nodes/Ports/Fibers/SRLGs
Simulate traffic/packet links passing the objects & check if succeed
Output failed traffic & Packet links affected by failure objects
Packet-Optical Topology& resources
Failure scenarios
The packet topolgy disconnection by dual fiber-cuts will cause partial flows fail to restore in that scenario
    Single failure or multiple failures combination
    Get Interrupted and restored packet Links/traffics
Notes: 六、What If 分析
1、输入是IP+光拓扑和故障网元或链路，输出的是中断的/恢复的业务和链路信息。
2、what if分析的主要目的是：对整个网络进行简易的故障模拟及分析。

## Slide 15: Optical topology & IP topology
    Optical topologies
    Generated packet topologies

## Slide 16: Simulation results - Two Layer Networks with Single Failure Protections
Protection Coordination | Top Layer Single Failure Protection | Bottom Layer Single Failure Protection | Dual Failure Restorability | Comments
None | Enabled | None | 41%-94% | 
None | Enabled | Enabled | 94%-99.7% | 
1+12

## Slide 17: No optical protection vs. Optical path protection
Fig. 2: the majority of the incompletely restorable scenarios will still have a large number of flows that are not restorable. The restoration on packet layer alone is not adequate for the dual failure protection;
Fig. 3: the small number of incompletely-restorable scenarios has large ratios on the service restorability. These values could help to evaluate the benefits of extra effort for protection coordination across layers;
Protection coordination: V. Liu, “Protection Coordination for Dual Failure on Two-Layer Networks,” in 11th Intl. Conf. on Design of Reliable Communications Network (DRCN), Kansas City, MO, USA, March 25-27, 2015.

## Slide 18: Future work - Multilayer coordinate protection
The capacity limitation on the dual failure resiliency
The capacity comparison of multilayer vs. two single-layer protection
Additional constraints for protection coordination across layers